## Slide 1: Patrol Boat Duty Basics
These slides were originally created to support SBSC Duty Training presentation. Hopefully they make sense in isolation and should at least act as an aide-memoire.
The Patrol Boat Duty is a key component in the delivery of safe and high-quality racing. These slides are designed to give the basics and provide a useful prompt, and we will seek to pair club members new to RIB duty with experienced drivers in order to gain confidence.
Please feedback anything you see that either causes you concern or you think could be improved via email: administrator@stokesbay-sc.co.uk.
Thanks and Good Luck!
Dan Vincent
Vice Cdre SBSC

## Slide 2: Set up - Patrol Boats
Pack all your warm, dry sailing gear – even in August
Arrive in plenty of time – 1000 latest.
Get boat out of garage
  Collect Key, Radio, First Aid and Race Kegs from Bridge
  Pick up Fuel ( fuel bunker key held in Bridge), check connection (Yellow has its own fuel tank)
  Buoys and ground tackle – careful when lifting heavy ground tackle – ask for help as required
  Run up engine – check water jet from cooling system.
Get Changed – Buoyancy Aid compulsory. Don’t forget suncream even in February
Radio check on shore
Launch – Kill cord on before engine start
Radio check on water.

## Slide 3: Patrol
Drop Racing Buoys – check position with RO.
Monitor Boats
In capsizes – count heads
  Ask first: Can crew self-rescue? Sailors in control.
  Ask what assistance is required?
  Full intervention take control – get crew into boat.
  Slow down until you need to speed up.
When close to people in water – engine awareness – position boat then cut engine (if in doubt pull kill cord)
Always prioritise people over boats
Communicate with Race Officer.

## Slide 4: Recover Patrol Boat
Confident drive onto trolley – in a strong tide stream you need sailors or crew to hold the boat. Watch fingers, legs.
Cut engine and raise
Secure to trolley
Tractor recovery – watch fingers and if in doubt shout ‘STOP’.
SIT DOWN if in boat when being towed.
Clear communication with tractor driver
Watch for beach users/ dogs/ children etc.
Rinse boat particularly trolley bearings, Flush seawater out of engine, radio
Return fuel, keys, radio, buoys to garages and lock them
Sign duty book, Record any faults in the defect book, get changed.

## Slide 5: Key Takeaways
Come prepared for the elements
Arrive early and get sorted/ changed quickly
Prioritise safety and communication with RO
Don’t switch off – monitor boats – take an interest
Recover boats, rinse and ensure everything is tidied away
Enjoy